Impact of Vietnam Industrial Production on Climate Change

Dr. Ngo Duc Lam, Chairman of Chemical and Industrial Safety Technology Institute (Vietnam Chemical Association)

I. Introduction: Climate change which is typical by the warming of atmosphere globally is one of the most concerned issues of the world environment. Reason for the increase of warming is the emission of greenhouse gases – such gases are released from human socio-economic activities, in which industrial production process and energy usage play a major role.

Presently, in Vietnam, the emission of greenhouse gases remains in low level, but in the near future, energy from fossil fuels will be used much more than today so the amount of greenhouse gases will also increase significantly and it is sure that this will contribute to the change in climate. Therefore research on impact of industrial production to climate change so as to inventory the emission amount and propose technical measures and policy to reduce the growth rate of greenhouse gas emission is a necessary issue.

II. The development of greenhouse gases in industrial production presently and forecasting the emission levels of greenhouse gases in the future.

Greenhouses gases in the nature mostly are steam, CO2, CH4, N2O, NOx, and O3. Gas is not of nature is Chlorofluorocarbons (CFC). Emission level of greenhouse gases mainly depends on economic and population growth rate in which industrial and energy activities are noteworthy.

In the industrial and energy activities, CO2 and NOx are released from the fossil fuel burning (coal, petrol) in the boilers of thermal power plants and in the incinerator of the cement, steel, paper, textile, and sugar and construction material plants.

In our country, it is noted that the greenhouse gases are also released from the coal, firewood, and agriculture by-products.

- Greenhouse gas emission from the power industry

Present condition and anticipation of the energy consumption in power sector

- In 1990:

+ Commercial energy consumption (kgOE/person): 63

+ Commodity energy consumption (KWh/person): 93

+ Energy intensity (KgOE/US$100): 344

- In 2002: The data are 208; 380; 512 respectively

- In 2003: Power sector consumed more than 3,070,000 ton of coal, 375,000 ton of oil and 2,983,000,000 m3 of gas. Power output from the plants, which used fossil fuel, is 22,000,000 Kwh, accounting for 54% of total power production with the rate of coal consumption from 330-818g/Kwh, and oil consumption from 366-376g/Kwh.

It is estimated that in the period from now to 2020, there has been additional 3500MW coal-fired power and 6750 MW natural gas power. In addition, the first nuclear power plant with capacity of 600MW-1000MW in Vietnam will be constructed.

So the consumption of fossil fuel up to 2030 is estimated as follows:

Table 1:

| Fuel | Year |
| --- | --- |
|  | 2000 | 2002 | 2005 | 2010 | 2012 | 2020 | 2030 |
| Coal (103 ton) | 2054 | 2679 | 4428 | 9815 | 11346 | 17474 | 46684 |
| DO oil (103 ton) | 493 | 383 | 71 | 41 | 43 | 0 | 0 |
| FO oil (103 ton) | 326 | 285 | 259 | 33 | 34.3 | 0 | 0 |
| Burning gas (103 ton) | 1224 | 2550 | 5001 | 8274 | 10425 | 16162 | 19054 |
| Total (KTOE) | 3075 | 4466 | 7309 | 11017 | 15814 | 24331 | 43292 |

- The emission of greenhouse gases from power production is as follows:

| Sector | Equivalent emission amount calculated by CO2 (103 ton) |
| --- | --- |
|  | 2000 | 2002 | 2005 | 2010 | 2015 | 2020 |  |
| Power | 11238 | 15270 | 21526 | 39791 | 63107 | 73448 |  |

Comments on technology in the production of coal-fired power and FO oil product

In general, productivity of our power equipment is still low. Recently, some new power plants have quite large productivity, so the average power productivity in Vietnam is about 60-70%. This figure is average productivity figure in the world – some equipment remains backward and old, the capacity of power unit is small, low parameters.

So, in order to reduce the greenhouse gas emission in the future, the policy chart for Vietnam Power development to 2020 is as follows:

- Do not develop direct FO-burning thermal power technology

- Choose burning chamber technology with have high productivity

- Have high and super-high pressure and temperature parameter

- Weed out old equipment

- Greenhouse gas emission from the cement industry

Cement is the industrial sector, which consumes the most energy (accounting for 17% of energy used for industry).

According to the general development chart of Vietnam cement, demand and cement output are estimated as follows:

Demand and Cement output

Table 3:

| Criteria | 2002 | 2003 | 2005 | 2010 | 2015 | 2020 |
| --- | --- | --- | --- | --- | --- | --- |
| Much growth | 20 | 15 | 13 | 10 | 5.8 | 2.5-3 |
| Demand 106 ton | 19.7 | 22.6 | 29 | 48.6 | 63-65 | 68-70 |
| Output 106 ton | 16 | 17.8 | 22 | 49.8 | 62.8 | 68 |

Forecasting the energy consumption of cement manufacturing sector

Table 4:

| Criteria | 2000 | 2010 | 2012 | 2020 | 2030 |
| --- | --- | --- | --- | --- | --- |
| Coal (ton) | 1,738,908 | 5,151,462 | 5,540,963 | 6,265,375 | 6,886,000 |
| Power (MWh) | 1,572,793 | 7,802,900 | 7,779,187 | 10,380,163 | 12,406,895 |

Greenhouse gases release from cement manufacturing process. Total greenhouse gas emission in cement manufacturing process including technology process, fuel burning, indirect from power consumption, and processing additive is presented in the following table:

Greenhouse gas emission in cement manufacture

|  | 2002 | 2005 | 2010 | 2015 | 2020 |
| --- | --- | --- | --- | --- | --- |
| Total waste (million ton of CO2) | 14.42 | 19.89 | 40.26 | 50.77 | 54.98 |

In order to reduce the emission of greenhouse gases in cement manufacture, we should focus on the measure of energy saving such as improving burning chamber, increasing the performance of making cool…, taking back the residual heat, shifting from wet process to dry process etc.

- Greenhouse gas emission in steel manufacture industry

Steel sector consumes much energy, only after cement industry. Steel sector consumes about 7.7% of energy used for industry and it is the sector which consumes the most electricity – in present, technology for manufacturing steel in Vietnam remains backward, the rate of energy consumption is still high, productivity is only 50% of energy consumption.

Steel productivity in Vietnam in 2002

| - Cast iron from iron | 50,000 | Ton/year | (From furnace stand) |
| --- | --- | --- | --- |
| - Steel alloy | 500,000 | Ton/year | (from electric furnace) |
| - Bridge and construction steel | 1,600,000 | Ton/year | (liquid roll, cold roll) |
| - Coated steel, pipe | 100,000 |  | (cast, roll) |

And the correspondence greenhouse gas emission is 3,355,800 ton of CO2.

- Greenhouse gas emission in paper manufacture industry

Estimating energy consumption in paper and pulp sector

Table 6:

| Criteria | 2010 | 2012 | 2020 | 2030 |
| --- | --- | --- | --- | --- |
| Gasoline (ton) | 96 | 108 | 172 | 308 |
| FO (ton) | 192,909 | 221,730 | 386,996 | 776,354 |
| DO (ton) | 20,084 | 23,037 | 39,880 | 79,187 |
| Coal (ton) | 594,532 | 684,503 | 1,132,126 | 2,290,247 |
| Electricity (MWh) | 862,378 | 1,009,607 | 1,897,557 | 4,171,028 |

Greenhouse gas emission in 2000-2002

Table 7:

| Year | Gasoline (t) | FO (t) | DO (t) | Coal (t) | Electricity (t) | Total |
| --- | --- | --- | --- | --- | --- | --- |
| 2000 | Energy consumption (t) | 50 | 75,583 | 9,742 | 302,105 | 414,383 |  |
|  | CO2 emission (t) | 124 | 244,889 | 30,785 | 647,862 | 254,845 | 1,228,150 |
| 2002 | Energy consumption (t) | 57 | 86,878 | 11,198 | 347,239 | 416,242 |  |
|  | CO2 emission (t) | 147 | 218,475 | 35,386 | 802,122 | 256,019 | 1,375,149 |

- Synthesizing the emission of greenhouse gases in industrial production presently and forecasting the amount of greenhouse gas emission in the future.

Economic growth rate in Vietnam is quite high with GDP from 7.5 – 8.5% / year, so Vietnam industry also has the growth rate of 14 – 16%/ year – demand of energy for industrial production is very high.

The increasing orientation of using energy from coal, oil and gas is presented in the following general energy table:

Table 8:

| Fuel | Year |
| --- | --- |
|  | 2000 | 2002 | 2005 | 2010 | 2012 | 2020 | 2030 |
| Coal (103 ton) | 2054 | 2679 | 4428 | 9815 | 11346 | 17474 | 46684 |
| DO oil (103 ton) | 493 | 383 | 71 | 41 | 43 | 0 | 0 |
| FO oil (103 ton) | 326 | 285 | 259 | 33 | 34.3 | 0 | 0 |
| Burning gas (103 ton) | 1224 | 2550 | 5001 | 8274 | 10425 | 16162 | 19054 |
| Total (KTOE) | 3075 | 4466 | 7309 | 11017 | 15814 | 24331 | 43292 |

Source: Energy Institute

EMISSION OF GREENHOUSE GASES IN INDUSTRIAL PRODUCTION PRESENTLY AND FORECASTING THE AMOUNT OF GREENHOUSE GAS EMISSION IN THE FUTURE

EMISSION

Table 9

| Sector | Year |
| --- | --- |
|  | 2000 | 2002 | 2002 | 2010 | 2015 | 2020 |
| Emission from coal exploitation process | 1016 | 1391 | 1515 | 2106 | 2400 | 2696 |
| Emission from oil exploitation and transportation | 54 | 55 | 59 | 72 | 73 | 60 |
| Emission from gas exploitation and transportation | 238 | 11 | 974 | 1596 | 2529 | 2677 |
| Power sector | 11231 | 15270 | 21526 | 39791 | 63107 | 73448 |
| Industry | 14081 | 17857 | 24754 | 35597 | 48126 | 64335 |
| Agriculture | 1124 | 1269 | 1386 | 1479 | 1757 | 2083 |
| Transportation | 11190 | 14737 | 1896 | 3088 | 43839 | 62594 |
| Trade and services | 3167 | 3712 | 4354 | 6001 | 8066 | 9831 |
| People’s activities | 3307 | 4286 | 4922 | 5767 | 6414 | 7823 |
| Total | 45121 | 58526 | 77426 | 121628 | 173712 | 222813 |
| Industry + power sector | 25312 | 33127 | 46280 | 75388 | 111233 | 137783 |

STRUCTURE AND GROWTH OF GREENHOUSE GAS EMISSION BY ECONOMIC SECTORS IN 2002-2020 PERIOD

# YEAR 2002

# YEAR 2020

Following comments can be made from the above tables and charts:

+ Greenhouse gas emission in our country is largest in energy, industry and transportation sectors (make up 90%) in which industry and energy sectors accounting for more than 60% and this tendency does not change up to 2020.

+ CO2 emission rate from agricultural and industrial activities in 2002 was not as high as in 1998. However, such rate in following years has increased much: 1.35, 1.7, 2.8 and 9 times in 2002, 2005, 2010 and 2030 respectively.

III. Some measures to minimize the growth rate of greenhouse gas emission in industrial and energy sectors.

In fact, the amount of greenhouse gas emission in Vietnam is not large compare with developed countries. However, it is noteworthy that the growth rate of greenhouse gas emission in recent years and the forecasted amount of greenhouse gas emission in the future is very high together with the socio-economic development. In order to reduce such emission, we should:

- Regarding management: Raising public awareness on climate change due to greenhouse gas emission in industrial and energy sectors. The government should have its policy so all the economic sectors shall pay attention to having effective measures to limit heavy emission.

- Regarding technique and technology.

- Implement well the policy on energy saving.

- Use effectively the primary material source, especially coal. In order to achieve this, it is needed to innovate equipment, mainly boilers and industrial furnaces, replace backward technological equipment by advanced and energy - saving technology.

- Use and exploit rationally new energy resources, clean energy such as hydraulic power, wind power, solar power, biological gas, etc.

- Using more associated gas in order to reduce the usage of coal as a kind of fuel at present.